## Slide 1: Introduction to: Files, Filesystems, and Disks
Moshe Caplan
moshecaplan@isis.poly.edu
Winter 2012

## Slide 2: What is a File?
Questions:
  How are files stored?
  How do we retrieve them?
A computer file is a block of arbitrary information, or resource for storing information, which is available to a computer program and is usually based on some kind of durable storage. A file is durable in the sense that it remains available for programs to use after the current program has finished. Computer files can be considered as the modern counterpart of paper documents which traditionally are kept in offices' and libraries' files, and this is the source of the term.
--Wikipedia
Definition obtained from: http://en.wikipedia.org/wiki/Computer_file

## Slide 3: How are files stored?
At a low level, files are stored as a bunch of bytes on a hard drive (or other storage media)
However, hard drives don’t understand “files”
  Hard drives simply contain a huge collection of bytes of data
We need some way to retrieve the bytes composing our file from the hard drive
  That’s where filesystems come in

## Slide 4: Human vs. Hard Drive View of a File
Left Side: Hard Drive View
  Actually, data would be further converted from hex to binary (1 and 0)
Right Side: Human View
  Data is converted into human readable characters

## Slide 5: Filesystems

## Slide 6: Filesystems
A filesystem is the middleman between users who only understand files and disks that only understand bytes and addresses
Responsible for organizing the data on a disk
  To ensure efficient storage and retrieval
Data organized in a hierarchy of files and directories
Analogy: Filing system in a medical office
  Files organized by last name to promote efficient storage and retrieval

## Slide 7: More about Filesystems
Filesystems are OS dependant
Responsibilities
  Creating files
  Deleting files
  Retrieving files
Generally, a filesystem will maintain an index of files
  The index contains the name of the file, address of the actual data blocks, and other useful info
  The index is similar to a phone book
  The index is also stored on the hard drive

## Slide 8: Common Filesystems
Windows
  FAT32
  NTFS
Apple Mac
  HFS
  HFS+
Linux
  ext2
  ext3
DVD
  UDF
USB Drives
  FAT32

## Slide 9: Example Filesystem: FAT32
Overview
  Really just a version of the FAT filesystem
    Other versions are FAT12 and FAT16
  One of the most simple filesystems
  Usage:
    Older versions of Windows (before XP)
    USB Drives
    Digital Camera Memory Cards

## Slide 10: FAT32
Components
  FAT (File Allocation Table)
  Data Blocks
  Directory Entries
    Stored within the data blocks
Layout of a drive using FAT32:
  Reserved Area contains filesystem information
Reserved Area | FAT | Data Blocks

## Slide 11: FAT32 Data Structures (1)
FAT (File Allocation Table)
  Maintains allocation status of each data block
  Links each block with the following block in large files
    There is one entry for each data block in the filesystem. That entry contains the location of the following block in a given file or indicates that it is the last block in the file.
  There is a primary and backup FAT

## Slide 12: FAT Data Structures (2)
Directory Entries
  Contains file name, size, metadata, and starting address of file contents
  Stored within the data blocks
  Analogy: Phone Book
Data Blocks
  Clusters containing the actual file contents

## Slide 13: FAT File Allocation (1)
Directory Entry Added
  Containing file name and location of first cluster
Data Blocks Allocated
  Number of blocks depends on file size
FAT Updated
  Each entry points to the next block of the file

## Slide 14: FAT File Allocation (2)
Image Obtained From: http://digital-assembly.com/technology/research/pubs/ieee-spm-2009.pdf

## Slide 15: Related Topics
Volume Layout – Partitions
PC Boot Process
Memory vs. Hard Disk

## Slide 16: Volume Layout - Partitions
A disk can be split up into multiple sections
  Each section is called a partition
    Ex. On Windows your “C” and “D” drives are each a partition
    Each partition can have a different filesystem
MBR (Master Boot Record)
  Generally in first 512 bytes (first sector) of volume
    Boot Code
    4 Entry Partition Table
      Specifies the partitions on the volume
  More information on the MBR (including layout) can be found at:
    http://en.wikipedia.org/wiki/Master_boot_record
MBR | Partition 1 | Partition 2

## Slide 17: Viewing the MBR (1)
One of the easiest ways to view the contents of the MBR is using the “mmls” command
  A component of “The Sleuth Kit” (TSK)
    http://cyfor.isis.poly.edu/modules/tsk-autopsy
  You will need to specify the volume you are looking at.
    On Linux it will generally be /dev/sda
You could also look at the first 512 bytes of a disk (see video)
DO NOT MODIFY ANYTHING IN THE MBR
  Your computer may not boot if you do

## Slide 18: Viewing the MBR (2)
CERT ADIA MBR
128 MB Flashdrive MBR

## Slide 19: PC Boot Process
Power On
BIOS (Basic Input Output Sequence)
  Hardcoded into the firmware
  POST (Power-On Self-Test)
    Identifies and Initializes System Devices
      Hard Drive, Keyboard, Video Card, etc.
BIOS finds a non-volatile bootable device
  Generally your hard drive
Loads the boot sector and passes off control
More detailed discussion:
  http://www.webopedia.com/DidYouKnow/Hardware_Software/2004/BootProcess.asp

## Slide 20: Memory vs. Hard Disks
Two types of storage on a computer
  Hard Disk
    Long term storage
    Non-Volatile (Can retain data without power)
  Memory
    RAM
    Temporary storage
    Volatile (Can’t retain data without power)
    Stores things that are currently being used
      Files being presently modified
      Open programs
      Running processes